## Slide 1: Lane Detection
CSE464 – Term Project
Team Members: Ahmet Yiğit, Özcan Akay
Instructor: Doç. Dr. Habil Kalkan
12/2024

## Slide 2: Introduction
Project Topic
Motivation
Methodology
Compression of Methodology
Results and Outputs
Conclusion and Future Work
References

## Slide 3: Project Topic
Line Detection:
  Image processing techniques for detecting lines.
Edge Detection:
  Sobel and Canny methods comparison.
Hough Transform:
  Geometric line detection.
Noise Reduction:
  Enhancing image quality for better detection.

## Slide 4: Motivation
Autonomous Driving:
  Accurate lane detection is crucial for navigation.
Robotic Vision:
  Essential for path planning and obstacle detection.
Real-World Challenges:
  Handling noise, lighting variations, and fragmented edges.
Industrial Applications:
  Used in quality control and automation systems.
Scalability:
  Potential for extension to curved lanes and complex environments.

## Slide 5: Methodology – Canny Edge Detection
Steps
  Noise Reduction: Applied Gaussian Blur to smooth the image.
  Edge Detection: Used the multi-step Canny algorithm for precise edge detection.
    Gradient Calculation
    Non-Maximum Suppression
    Double Thresholding
    Edge Tracking by Hysteresis
  Line Detection: Employed Hough Transform to identify accurate lines.

## Slide 6: Methodology – Canny Edge Detection
Advantages
  Sharp and accurate edge detection.
  High performance in noisy environments.
Disadvantages
  Higher computational cost.
  Sensitive to lighting variations.

## Slide 7: Methodology – Non-Canny
Steps:
  Noise Reduction: Used Gaussian Blur to smooth the image.
  Edge Detection: Detected edges using the Sobel filter for gradient calculations.
  Line Detection: Applied Hough Transform to extract lines.
Advantages:
  Faster processing time.
  More stable under varying lighting and environmental conditions.
Disadvantages:
  More sensitive to noise.
  Less precise edge detection compared to Canny.

## Slide 8: Compression of Methodology
Feature | With Canny Edge Detection | Without Canny Edge Detection
Noise Reduction | Gaussian Blur | Gaussian Blur
Edge Detection Method | Multi-step Canny algorithm | Sobel filter for gradient calculations
Line Detection | Hough Transform on refined edges | Hough Transform on Sobel-filtered edges
Advantages | - High accuracy - Robust to noise | - Faster processing - Stable in varying conditions
Disadvantages | - Sensitive to lighting - Computationally intensive | - Less precise - Sensitive to noise
Best Use Case | Applications needing precision (e.g., medical imaging) | Real-time and general-purpose tasks (e.g., autonomous driving)